## Slide 1: Marine Induced Polarization A New Electrical Water-Pollution Detection Technology
Mike Williamson, Jeff Frank, Herb Barrow
Jeff Wynn

## Slide 2
USGS Marine Induced Polarization Technology (Marine IP)
HISTORY
Induced Polarization (“IP”)
  first observed by Conrad Schlumberger in 1912
  first published in 1920.
Marine IP: Developed by the US Geological Survey.
Two patents for mineral mapping awarded 2001;
Third Patent for oil-hunting awarded in 2013;
SEA-TRIAL LOCATIONS
1Virginia
2Savannah, GA
3Egmont Shoals SW Florida
4Biloxi-Gulfport, MI
5Cape Fear, NC
6Bismarck Sea
7South Africa
8Puget Sound
9Couer d’Alene River, ID.

## Slide 3: The physical mechanism(s)
Marine IP – How it works
Measuring the charge induced on certain particles in a conductive electrolyte (water) within an inducing electric field
DETECTION LEVEL: Sulfides to 0.04%, FeTiO3 to 0.01%, Oil to 0.0002%
(Sometimes called the Double-Layer or Warburg Effect)
-
+

## Slide 4: How it’s done…
Marine IP – How it works
IP is a change of resistivity with changing frequency
Ground or Sub-Seafloor
Current Source
Receiver Voltage

## Slide 5
Marine IP – How it works
What does it LOOK like?
IP is now typically measured as a
phase-shift.

## Slide 6
Marine IP – How it works
A KEY POINT: IP is a SURFACE-sensitive phenomenon
Think: A bar of silver vs. silver coins scattered over the sea-floor beneath a sediment-cover.

## Slide 7
x
Smith Shoals
…plus Bismarck Sea, South Africa, Puget Sound
Notes: I conducted initial marine IP sea-trials at five different locations around the southeastern USA. Note the huge potential offshore titanium resources (warm colors; they stem from a huge USACE vibracore survey). Active mining of titanium is taking place in Florida and New Jersey.

## Slide 8
Marine IP results, South Africa Offshore Survey -
The largest IP survey in history.
Survey area:
3.5-4.5 km x 11 km
…at 100-m spacing
830,000 Induced Polarization measurements in 25 operational days
A typical land-based IP survey can acquire 50-75 stations per day
South Africa Offshore Survey
TWO vast, previously undiscovered titanium deposits.
Notes: N = 1 is the shallowest depth – in this case where most of the titanium oxide is located. The array can detect ilmenite to at least 20 meters.

## Slide 9
How deep into sediments can we “SEE”?
Effective sampling to depths of 20+ meters
Notes: This figure shows how resolution diminishes with increasing depth.

## Slide 10
In 2010 something caught everyone’s attention.
Notes: The Deepwater Horizon blowout, April 2010.

## Slide 11
There has just GOT to be something better than dragging a diaper-covered ball-anchor on a chain through water to look for drifting or sunken oil!*
* Columbia River ~ 20 years ago.
Notes: Older means for tracking oil on the seafloor involved dropping chains and cannon-ball anchors wrapped in Huggies to see if a point on the river floor or ocean floor had any oil on it. Really. Using U/V light on a sensor towed through the water detects oil up to 2 cm away… but the sensor is then fouled and thus compromised by that oil.

## Slide 12
A thought-experiment: the IP effect is capacitive in behavior…
Oil in seawater should behave the same.
To address this, start with a topological equivalency…
Notes: This is the critical conceptual step: the topological equivalency.

## Slide 13
This is the first laboratory IP configuration set up for oil.
…so I decided to experiment with detection of dispersed oil…
Titrating multi-vis oil into...
seawater
Receiver
Transmitter
Four-Mesh Electrode (Wenner) Sample Cell

## Slide 14
…these results beat ALL expectations.
Hydrocarbons in seawater gave the strongest IP response EVER:
Notes: This is HUGELY significant. It means we can track and quantify a dispersed oil plume in real time, but that we can also estimate the average droplet-size. This latter means we can actually monitor bio-degradation as it is taking place. Another hugely significant point: on land a 4-person crew can make about 100 IP measurements in a day. With the South Africa array we were measuring 50,000 stations a day.

## Slide 15
We set up a more sophisticated laboratory in Seattle…
…and we can now detect hydrocarbons down to 2 ppm
[We’ve started lab experiments with dispersants and oil combinations.]
Notes: This is a more sophisticated laboratory designed to track behavior of oil and dispersants in sediments in the most realistic manner possible... Short of dumping some nasty stuff into a river or estuary or Sound somewhere.

## Slide 16
One of several possible configurations for the deep ocean
Notes: This sort of array could in theory sample the entire seawater column. Towed in parallel paths (“lawn-mower fashion”) it can provide a 3D image of where hydrocarbons are located.

## Slide 17
The South African Array achieved a depth-penetration of 20+ meters
A River-Bottom or Seafloor configuration.
Investigation range is primarily dependent on electrode spacing:
The trade-off is thus Resolution vs. Depth of Penetration
Notes: For a large (15m here) array spacing, we can “see” more than 20 meters below the seafloor, but have correspondingly less resolution. A hybrid streamer design will allow us to get both depth AND resolution, however.

## Slide 18
Eagle Harbor Superfund Site, Puget Sound
Seattle
Former Wyckoff Plant
Google Earth
Ferry Terminal
August IP
Profiling
Calibration
Profiling
Run 6 South

## Slide 19
…By 1994, EPA had removed 29,000 tons of creosote
sludge, 100,000 gallons of oil, 430 square yards of asbestos,
and a block of almost-pure naphthalene the size of a small car.
In the following eight years, they also treated 370 million
gallons of groundwater and removed 100,000 gallons of
non-aqueous phase liquids (NAPL).
However, it is estimated that approximately a million
gallons of NAPL remain at the site…
The Eagle Harbor/Wyckoff Site
IP Trials
A wood-treatment plant operated here for 85 years; it
was declared a Superfund site in 1987. The wood-treatment
process involved PAH’s, PCP’s, carrier oils, & dioxins/furans.

## Slide 20
A FULL list of all the 86 contaminants runs four pages long, including oils, furans, PAH’s, and even heavy metals…

## Slide 21
And stuff like this keeps popping up from the sand-cap…

## Slide 22
Eagle Harbor/Wyckoff Data gathered on 13 December 2016
N-S line detected anomalies within the cap area scheduled to be patched and in southern extension
East Beach attempt at reciprocal lines showed spatial consistency, differing phase shift values due to cross line offsets most likely caused by change in tidal current vector(approaching and ascending slack)
Processing noise thresholds set high due to leakage in the cable limiting capture of higher harmonics; still able to recover meaningful data
Based on initial August Wyckoff trial, transmit amperage was greater (12amps vs 4amps)
East Beach comparative results from the August and December trials show good correlation
East Beach results tie well with TarGOST data and core sampling programs
Tar-specific Green Optical Screening Tool (TarGOST®). Used in detection of coal tars, creosotes, heavy crudes, and tank bottoms.
Anomalies need ground truthing with the current Wyckoff sample database collected within the target area
Run 6 South
Observed scours
in the cap
Blue: Shallowest depth
Red: Next deeper depth
(of four depths acquired)
56 Hz
72 Hz
We can collect data for 4 - 6 layers/depths at the
same time as fast as we can tow the active streamer

## Slide 23
A Replication Check:
Bingo: The system replicates

## Slide 24
A Comparison Check with the EPA TarGOST Survey
…AND we get anomalies at the same places.

## Slide 26
Kalamazoo River
Perspective: Kalamazoo River DilBit Spill, 2010: $1.2 Billion
Notes: 1.2 billion dollar clean-up effort diluted bitumen (heavy tar sands)
A reasonable case can be made that IP would have had a significant impact on cost reductions in the clean up effort

## Slide 27
The Take-Aways – Marine IP:
Satisfies the OSRO Guidelines with respect to Non-floating oil recovery.
Can map hydrocarbons in the open water-column.
Can map oil and similar materials sequestered in river and ocean sediments.
FAST and cheap – 5-6 depths * 16 samples/second.
Can be done using a 23-ft boat.
Detection is SURFACE (not volume) sensitive.
Responds strongly to pipelines, cables, buried wrecks.
(We’ve seen cables & two buried wrecks so far).
Provides fast 3D imagery (so-called “layer hot maps”).
Is non-intrusive (relevant for Superfund sites).

## Slide 28
Peer-Reviewed Scientific Bona-Fides:
This paper in Ocean Science describes the hydrocarbon- mapping technology:
Notes: A peer-reviewed academic journal article on the concept of using seawater capacitance (previously considered an oxymoron) as a proxy for mapping and characterizing hydrocarbons in rivers and ocean water.

## Slide 29
An invited feature article in Sea Technology magazine gives some basic background for Marine IP, including how easy and fast it is to employ:
Notes: A peer-reviewed general publication describing the marine IP technology.